## Slide 1
HARMAN International. Confidential. Copyright 2018.
HYPERVISOR BASICS
October, 2023

## Slide 2: AGENDA
Why do we need a Hypervisor?
What is Virtualization? What kind of Virtualizations?
Virtualization goals
Types of Hypervisor and Advantages
Virtualization in ARM architecture
RB (Harman) Hypervisor overview
High level view of QNX hypervisor

## Slide 3: WHY DO WE NEED A HYPERVISOR ?
Deployment of popular Android ecosystem in an In Vehicle Infotainment (IVI) head unit along with Safety critical time sensitive applications running on a Real time operating system on a single SOC with shared peripherals.
Multiple SOC
Not an option as its costly
Container
Is possible system has a common kernel. But common kernel can be a blocker
Hypervisor
Ability to run multiple OS on the same SOC

## Slide 4: WHAT IS VIRTUALIZATION?
Virtualization is the creation of a virtual -- rather than actual -- version of something, such as an operating
system, a server, a storage device or network resources. By definition it is isolated computing environment(s) on the same physical computing platform.
Began in 1960, as a method to divide system resources between different applications in mainframes.
Virtualization hides the physical characteristics of an actual platform from the users/ guests, presenting instead another abstract computing platform. The software that controlled virtualization was called a "control program", but later came to be known as the terms "Hypervisor" (kernel is called the “Supervisor” and this manages them – hence the term) which hosts isolated computing platforms (could be heterogeneous i.e. not all are of same type) called “Virtual Machine" or “vPlatform”.
* Definition taken from Wikipedia : https://en.wikipedia.org/wiki/Virtualization

## Slide 5: GOALS OF VIRTUALIZATION
Isolation: At its core, virtualization provides isolation between virtual machines running on a single physical system. This isolation allows the sharing of a physical system between heterogeneous, mutually distrusting computing environments. For example, two competitors can share the same physical machine in a data center, using two different OS without being able to access each other’s data. The Hypervisor prevents any non trusted guestOS from interfering with trusted and real time guestOS and also ensures KPI of the RTOS.
Sandboxing and security / safety: VMs can be used to provide sandboxes for applications that might interfere with the rest of the machine that they run on. Examples of such applications include legacy applications, or software that is in development. Running those applications in a VM prevents bugs or malicious parts of the applications from interfering with other applications or data on the physical machine.
High Availability: Virtualization allows seamless and transparent migration of workloads between physical machines. This technique is commonly used to migrate workloads away from a faulting hardware platform that may require maintenance and replacement.
Workload balancing: To optimize the hardware and power budget of the data center, it is important to use each hardware platform as much as possible. Again, this can be achieved using migration of virtual machines, or by co-hosting suitable workloads on physical machines. This means that the physical machines are used for as much of their capacity as possible. This provides the best power budget for the data center provider, and the best performance for the tenant.
.

## Slide 6: TYPES OF VIRTUALIZATION
Full Virtualization: In full virtualization, the virtual machine monitor simulates the required hardware to allow an unmodified "guest" OS to be run in isolation. The “guest” does not know that it is running on a virtualized environment.
Para-Virtualization: In para-virtualization, the “guest” OS is modified to run in the virtualized environment. i.e. the drivers are virtualization aware. This means, that the source code of the OS needs to be available and modifiable. Typically, the HYP / Host OS side drivers are called Back End (BE) and Guest OS side drivers are called Front End (FE).
  Virtio based Virtualization: It’s a standard virtualization technique, using Para Virtualization, but the Linux kernel based guest OS FE drivers are standardised and mainlined to upstream kernel. Also, for many known hypervisor configurations, BE driver ports are available. Thus, the guest OS can simply enable certain virtio configurations and without any other modification in guest, can leverage the performance benefit of Para Virtualization compared to Full Virtualization.
Hardware Assisted Virtualization: In hardware assisted virtualization, the hardware is aware of the virtualization and therefore, the VMM leverages the available support. The unaware guest OS can run “unmodified” for most part. This takes the advantages of both full virtualization - where guest OS modifications are minimal and para virtualization – where performance is better. In fact the performance is much better while using HAV.
8

## Slide 7: TYPES OF HYPERVISOR
TYPE 2 (Hosted)
Hypervisor itself is hosted by another operating system, called Host OS
Ex: Oracle VirtualBox, IBM VMWare
TYPE 1 (Standalone / Bare Metal)
Hypervisor (Nanokernel) runs in “Hypervisor” mode or in a more privileged mode than kernel and directly
controls all HW access
Ex: XEN (OpenSource), RB (Embedded HV)
TYPE 1.5 (??)
Microkernel based OS with hypervisor extensions.
Ex: QNX, KVM(often called Type 2)
Micro Kernel based OS with Hypervisor Extensions
Android / Linux

## Slide 8: Advantages of Type-1 & Type 1.5 Hypervisor
Type 1 & Type 1.5 Hypervisor can be expected to provide the right performance – e.g., no significant degradation of boot time, interrupt latency, scheduling / task switching latency, etc. because it operates as a thin nano or micro-kernel layer directly on top of the HW just exposing hardware resources to Guest OSes.
Boot time of Guest in Type 1.5 Hypervisor is more than Type 1 Hypervisor, because in case of Type 1.5 Hypervisor, both Host domain & Hypervisor comes first then Guest domain.
Both Type-1 & Type 1.5 Hypervisors can make an RTOS and an HLOS co-exist with required isolation and security within the same CPU.
Both Type-1 & Type 1.5 Hypervisor can enable Hardware Pre-emption (=Hardware Requisition) as demanded by Real Time, Rear-View camera Use Case.
Both Type-1 & Type 1.5 Hypervisors can leverage the Hardware Virtualization Extensions and / or Hardware Assisted Virtualization to the fullest and run a Guest OS with less paravirtualization.
Type-1 and Type 1.5 Hypervisors are used more on Embedded and Soft Real Time Systems.

## Slide 9: ARM Arch (AArch64) Virtualization support, HAV extensions – Exception model
Execution Privilege / Exception Level
Access to System and Processor resources are segregated among different software modules. Not everyone can access everything. This is called ‘Execution Privilege’ (PL).
The ‘Current Privilege Level’ (CPL) can change only when an ARM Processing Element (PE) (or more commonly known known as a Processor Core) takes or returns from an Exception. Thus in AArch64 terminology PL is actually called Exception Level EL(x), where x = [0, 3]. EL0 is least privileged and EL3 is most.
The Exception can be Asynchronous (generated out of sync of instruction stream) and also called Interrupts. This are generated by HW peripherals.
Synchronous exceptions are generated during instruction execution. These could be because of some specific instruction execution like ‘svc’ to change to kernel mode or ‘hvc’ to change to hypervisor mode; could be because of configured instruction traps (traps = generate exception on executing certain instruction / accessing register); could be by Memory Management subsystems (MMU) faults.

## Slide 10: ARM Arch (AArch64) Virtualization support, HAV extensions – CPU and System Register virtualization
pCPU and vCPU
Each VM is assigned a set of virtual CPU or PE called vCPU. Each of them could be bound (pinned for all the time or dynamically scheduled for a given quantum of time) to a physical pCPU by the Hypervisor.
Special instructions which could modify System or CPU states are configured to be trapped by HYP. So that, when such instructions are executed by a guestOS, an exception is generated to EL2 and HYP emulates the behaviour of the instruction as it wants (and the guesOS can’t arbitrarily control system behaviour). Like the PSCI or SCM instructions.
System Register Virtualization
ARM registers are classified in System registers – those are used to get and set system configurations like control and status reporting, and General Purpose registers – those are the data registers for programmers. System registers are often ‘banked’ for different EL (i.e. similar function of such register is physically different for each EL and have different instruction encoding to access it). These are suffixed as _ELn, and the suffix indicates the minimum privilege required from which EL this register is accessible. Example SCTLR_EL1, _EL2 and _EL3 – system control register for each EL to configure MMU, cache etc.
HYP emulation via instruction trap is not efficient for frequent operations. For many such cases, for which the HYP needs to present an emulated view, the arch provides dedicated virtualized registers which can be directly read by the VM. The HYP usually programs such registers on startup – how values will be derived for those register access by a VM, from the corresponding original register. Usually these are prefix by ‘V’. Like VMPIDR_EL2: is the value to return for EL1 reads of MPIDR_EL1 (to get the CPU core affinity).

## Slide 11: ARM Arch (AArch64) Virtualization support, HAV extensions – Interrupt virtualization
Handling exceptions are tricky in virtualized systems. Some need to be routed to the HYP itself and handled there. Some could be coming from resources directly assigned to a VM and need to be routed there for handling. Also, it could be possible that, the VM for which the interrupt is targeted is not running at that point. So, HYP effectively needs Arch support of IRQ configuration, masking, routing to specific PE, interrupt generation and forwarding etc.
ARM Arch provides support for HYP control of IRQ through configuration register HCR_EL2. Also, ARM provides Arch support for Virtual IRQ (vIRQ) generation and management through HCR_EL2 and through ARM GICv2 onwards.
vIRQ can be generated by HYP programming the HCR_EL2 as and when needed. But this requires that HYP emulates the GIC functionality for the vIRQ it generates (the context management, masking, routing etc.) – which is a bit inefficient to do in software for interrupt handling.
So, ARM also provides Arch support of vIRQ request and management through the GIC as shown in the figure. This is efficient and does not have the previous software emulation performance problem.

## Slide 12: ARM Arch (AArch64) Virtualization support, HAV extensions – Traps and Emulation
Sometimes a hypervisor needs to emulate operations within a Virtual Machine (VM). For example, software within a VM might try to configure low level processor controls relating to Power Management. Typically, the VM should not be given direct access to these controls, because they could be used to break isolation, or to affect other VMs in the system.
A trap causes an exception when a given action, such as reading a register, is performed. The hypervisor needs the ability to trap operations, like the ones that configure low level controls, in a VM and emulate them, without affecting other VMs.
The architecture includes trap controls to trap operations in a VM and emulate them. When a trap is set, performing a specific action that would normally be allowed causes an exception to a higher Exception Level. The hypervisor can use these traps to emulate operations within a VM.
For example, executing a Wait For Interrupt (WFI) instruction usually puts the CPU into a low power state. By asserting the TWI bit, if HCR_EL2.TWI = 1, then executing WFI at EL0 or EL1 will instead cause an exception to EL2.
An OS would usually execute a WFI as part of an idle loop. With a Guest OS within a VM, the hypervisor can trap this operation and schedule a different vCPU instead.

## Slide 13: ARM Arch (AArch64) Virtualization support, HAV extensions – 2nd stage MMU
When HYP i.e. EL2 is enabled, ARM Arch provides support for a MMU 2nd stage which is under control of the Hypervisor. It allows the hypervisor to control which memory-mapped system resources a VM can access, and where those resources appear in the address space of the VM. Stage 2 translation can be used to ensure that a VM can only see the resources that are allocated to it, and not the
resources that are allocated to other VMs or the hypervisor.
1st stage MMU is under control of EL1, i.e. VM kernel and it maps the Virtual Address (VA) to Intermediate Physical Address (IPA).
2nd stage MMU maps the IPA to Physical Address (PA) and enforces memory protection as configured by the HYP, using 2nd stage translation tables.

## Slide 14: ARM Arch (AArch64) Virtualization support, HAV extensions – 2nd stage MMU - Emulated Device in memory
HYP can emulate memory mapped IO (MMIO) registers of a “virtual” device using 2nd stage MMU.
Emulated IO ranges are marked to produce “fault” in the 2nd stage translation table. HYP catches them and in software implements the virtualized device logic. It can even manage (for concurrent access protection etc.) and route these to a physical device mapped at a different address, and visible only to HYP.
This allows emulation of some of the basic system devices which each OS would need and could be needed early. This also allows using unmodified drivers for those devices in guest OS. But this increase HYP footprint and also this emulation is costly in terms of performance. So only basic devices like system console, GIC, system timers are typically emulated by HYP.

## Slide 15: ARM Arch (AArch64) Virtualization support, HAV extensions – 2nd stage MMU for DMA transactions (SMMU or IOMMU)
Memory virtualization for which access originates from CPU is managed by the 2nd stage MMU or S2MMU. Memory virtualization management for which access is not originated by processor, like the cases of several DMA master IP, following problem could happen when EL2 is enabled:
Isolation: The DMA controller is not subject to the stage 2 tables, and could be used to breach the VM’s sandbox.
Address space: With two stages of translation, what the kernel believes to be PAs are IPAs. The DMA controller still sees PAs, therefore the kernel and DMA controller have different views of memory. To overcome this problem, the hypervisor could trap every interaction between the VM and the DMA controller, providing the necessary translation.When memory is fragmented, this process is inefficient and problematic.
So the 2nd stage MMU regime is extended for DMA masters and those IP are called System MMU or IOMMU and is programmable by the HYP.

## Slide 16: ARM References
Much of the previous slides are based off ARM documentation
https://developer.arm.com/documentation/102142/0100/Introduction-to-virtualization
https://developer.arm.com/documentation/102412/0103/Privilege-and-Exception-levels
https://developer.arm.com/documentation/101811/0103/What-is-memory-management-

## Slide 17: Redbend (Harman) Type-1 / Bare metal, Embedded Automotive grade HYP on Samsung Exynos Auto v920 SoC based platform
The HW Platform
Samsung EAv920 or derivative based SoC having upto 2 quad core and 1 dual core RISC Arm Cortex A78ae 5 nm silicon CPU clusters
16-24GB LPDDR4/5 and 128/256 GB UFS 3.1
With advanced GPU, NPU, Gigabit Ethernet, DSP, DSI/DP, CSI, PCIe, USB3, USI ports and GPIOs. Cortex R52 cores for Safety apps
Used as Automotive Integrated Cockpit Domain Controller ECU cluster hosting advanced ADAS + IVI applications for the Driver, Co-Passenger, Rear-Seat-Entertainment
Capable of running one RT patched Linux as main ASIL OS and Android based GPOS for IVI (mixed criticality system) with Arm TEE / TZ support
The Hypervisor is ASIL-B certified for Automotive safety

## Slide 18: The RB (Harman) Hypervisor
The Hypervisor is implemented as a thin (executes within 128 to 256 MB DRAM) and fast Nano Kernel (NK) component.
It runs off EL2 and EL2 context switch is governed by Exceptions, Traps, Hypercalls as shown in the figure.
The hypervisor by itself usually does not run as an active entity and does not provide any console by itself.
The hypervisor uses Device Tree (DT) as Hypervisor Configuration Block (HCB) for settings related to the Hypervisor itself, the devices it owns, the physical hardware platform, the devices it makes available to each guest OS / vPlatforms etc.
It supports debugging and profiling capabilities through ARM debug registers and counters. Also it has console and in-memory logging facilities.
In order to satisfy embedded bare metal cases to avoid latency, it uses pinned vCPU to pCPU configuration; and does not use floating vCPU scheduling. However, it supports CPU hotplug and migration (to another VM).

## Slide 19: The RB (Harman) Hypervisor – Virtualization Techniques: Device Emulation
The Hypervisor emulates the basic devices needed by each of the OS – because everyone needs them including the HYP itself.
Typically the GIC, UART console and Timers are emulated.
The hypervisor has drivers to emulate those devices in-memory and traps the access those devices from each VM and sends virtual interrupts to VMs from these emulated devices. HYP driver for these manages the access and routing to / from VMs and also with its own access for the real physical devices.

## Slide 20: The RB (Harman) Hypervisor – Virtualization Techniques: Device Pass Through (PT)
For the devices those are in multiple (like USI devices) or those are needed only by one of the VM – there is no need to share the same device among VMs.
For these the MMIO registers, the RAM reserves, the IRQs, the GPIO pins can be configured exclusively to the VM who needs it.
Once configured, HYP usually don’t intercept the access to this device from the granted VM. So the performance is identical to non-virtualized systems for these devices.
Also for these native drivers can be used.

## Slide 21: The RB (Harman) Hypervisor – Virtualization Techniques: HPT and MPT
There are two special types for PT:
  Hardware Assisted Pass-Through (HPT): The HW itself is capable of managing concurrent access from different VM. Typically the HW composes of multiple independent DMA channels and Host Controller Interface (HCI) registers, which can be individually PT to different VM. Thus once the MHCI is configured, with minimum inter vm control path communication through xIRQs and with dedicated HW IPC support (i.e. Mailbox) between HCIs, both control and data plane IO paths and IRQs can be routed through the specific VM independently. This provides extremely good performance. Used for UFS and Ethernet – since those are very performance critical.
  Mediated Pass-Through (MPT): The HW MMIO registers, memory regions, IRQs, IO pins are continuously re-assigned after a time window to another VM. This arbitration is done via inter vm communication through HYP between the BE and FE pairs of the ‘Arbitrator’ driver. This is like Time Domain Multiple Access via time slice sharing. So, in given window only one VM can natively access the device with full performance. Only the small overhead invoked is due to the arbitrator scheduling. This also provides nice performance and used for GPU virtualization.

## Slide 22: The RB (Harman) Hypervisor – Virtualization Techniques: Device Sharing via Virtual Driver pair (BE/FE)
For the shared devices, para virtualization is used. Physical device is configured in one of the VM. This is called the device Back End (BE).
Here, specific virtual driver called BE driver is used, which communicates with the physical device via the native driver and manages concurrent access from other VMs.
In other VMs where the shared access is needed, specific virtual driver called Front End (FE) is used, which is bound with the virtual device.
Both the data and control path communication happens via inter vm communications channels, typically built upon virtual interrupts (xIRQ) and shared memory (vLink).

## Slide 23: The RB (Harman) Hypervisor – Virtualization Techniques: Virtio Devices
Virtio, as mentioned earlier is device sharing technique by Para Virtualization, i.e. using virtual driver pairs (BE-FE)
In our platform, the virtio architecture is based off Google’s CrossVM / Trout implementation

## Slide 24: The RB (Harman) Hypervisor – Communication Channels
Though isolation is the key of virtualization, intercommunication between isolated components are inevitable. So, those communication channels should be properly controlled and checked by the Hypervisor.
Communication channels are there for inter VM communication, VM to HYP and vice versa, HW to VM and vice versa, HW to HYP and vice versa.
Cross IRQ (xIRQ) based off ARM vIRQ and shared memory (pMEM and pDEV) tied together form a basic communication entity for inter VM communication – it is called vLink. The pMEM is persistent (across VM reboot) buffer shared between two VM for a vLink. pDEV is persistent (across VM reboot) buffer private to a vLink endpoint. vLinks also could be between VM and the HYP. The pDEV and pMEM buffers are crafted out of HYP DRAM quota.
Using vLink as a base, several other high level inter communication protocols like vSock, vEthernet, vMQ, vRPC, vPIPE etc. are made available.
VM to HYP communication happens via Hypercall built upon ARM ‘hvc’ instruction (like the Systemcall i.e. ‘svc’ kernel interface). VM to EL3 happens via ‘smc’ instruction trap and emulation by Hypervisor.
HW to VM communication happens via Hyp taking the physical IRQ and forwarding the vIRQ. HYP to VM happens via the vIRQ (xIRQ).

## Slide 25: QNX HYPERVISOR – BIG PICTURE

## Slide 26: QNX HYPERVISOR – Cont.

## Slide 27: QNX HYPERVISOR – Cont.

## Slide 28: QNX HYPERVISOR – Cont.

## Slide 29: QNX HYPERVISOR – Cont.

## Slide 30: QNX HYPERVISOR – Cont.
HARMAN International. Confidential. Copyright 2015
14
eMMC is virtualized. Mechanism used is virtio-blk
Virtio is a virtualization standard used for virtualizing (sharing) block devices, network devices etc.Virtio is an example of paravirtualization technique, that uses virtual queue to enable communication between hypervisor and guest.
QNX
virtio-block backend driver is present on QNX. This driver interprets the commands/data sent by the virtio-frontend driver from guest VM, creates proper commands for eMMC controller, and forwards those commands to actual eMMC driver on QNX.
Android
Virtio-block frontend driver is enabled in Android kernel.This driver writes commands/data to the virtual queue, which is read by the virtio-block backend driver running in QNX.

## Slide 31: QNX HYPERVISOR – Cont.

## Slide 32: Linux Kernel Overview
Developed initially by Linux Torvalds and being maintained buy Open Source Kernel community
Runs in Kernel mode
Customization:
  Kernel is reconfigurable, compiled as per need
  Configurable via kernel config and Device Tree
  Cross compilation
Monolithic Type:
  Kernel modules can be in built or build as apart of insertable modules
Runs on HW or virtualized environment
Userspace applications running top of kernel in userspace mode
Modules to list a few
  Process Management or scheduling
  Memory management
  Power Management eg, S2R, CPUIdle, CPUFreq, runtime PM etc
  Peripheral drivers, E.g. USB, UART, I2C, SPI etc
  Multimedia E.g. Display and Graphics, Sound etc
  Connectivity E.g. WIFI, BT, Ethernet,

## Slide 33: Linux Kernel Architecture..

## Slide 34: Linux Boot Flow..

## Slide 35: THANK YOU
©2018 HARMAN INTERNATIONAL INDUSTRIES, INCORPORATED
22